Flood Risk Assessment

In Respect of Works to

5 Meadow Close

Sevenoaks

Kent TN13 3HZ

- The site location

  - The site is located on the south western side of Meadow Close cul-de-sac and is bounded to the west and south by residential gardens, to the north by private garages and to the east by Meadow Close roadway.

  - It falls within Flood Zones 2 and 3 according to the Environment Agency map.

  - The building is a three storey semi-detached building typical of the houses on the road.

  - The building is constructed of cavity brickwork walls with a pitched roof with concrete interlocking tile finish. The existing ground floor finished floor level is approximately 82.00 AOD.

  - The side and rear of the property is finished with a paved patio area and lawn to the rear of the garden. The front of the property is finished with a paved driveway. The surface water from the property drains into a public surface water sewer to the rear and front of the building within the site curtilage.

  - The strata is mainly sand below the topsoil level.

- The Proposed works

  - The proposed works comprise the erection of a single storey side and rear extension and single storey front porch that will increase the footprint of the building by 62.0 m2.  The majority of the extension will be on existing impermeable patio and concreted areas and therefore there will be minimum additional run off from impermeable areas.

  - The floor level will be the same as the floor level of the existing house. It would be neither practical nor reasonable to raise the floor level in this instance.

  - The extension will be constructed with cavity brickwork/blockwork to match the existing house on piled foundations and a reinforced concrete floor allowing water movement in the ground without affecting the new works.

  - The soft landscaping will remain as existing and made good to disturbed areas.

- Environment Agency standing advice.

  - In consideration of the Environment Agency`s standing advice and as mentioned above, the floor of the extension will be piled foundations and a reinforced concrete floor allowing water movement in the ground without affecting the new works.

  - The wall construction is shown to match the existing and we do not consider a different construction would be beneficial in this instance.

  - Surface water will discharge to the existing surface water public sewer.

End of statement

3rd March 2021

Append – EA flood map.