| 27 Upper Gordon Road Camberley Surrey GU15 2HJ Methodology | Dowling and Sons Facility Management & Maintenance 63 Pinehill Road Crowthorne RG47 7JP |
| --- | --- |
| Re-painting |
| Description of operation: |
| Removal of existing paint across all woodwork areas, window frames, doors and eaves and repainting using three coats as per materials statement. Scaffolding will be erected to appropriate UK health and safety standards to cover the house where repointing and repainting will be carried out by Seven Counties scaffolding company. Initial work to remove the chimney and do the repointing will take place prior to the painting works. The guttering will be removed and where items need to be replaced these will done after painting work is completed. Seal the guttering holes prior to removal of the paint phase. Where paint is loose or blistered it will be removed with scraper or manual hand tools as appropriate. The paint in the exterior of the windows and under the eaves will be removed to the wood to check for soundness. Delicate window work will require Nitromore to be used to remove paint from Georgian stiles windows and also from the stained glass windows. In cases where windows have been sealed with paint for security the paint will be removed to check the soundness of wood and windows painted to reseal and secure windows. In all cases, and particularly when using heat or vibration tools, extreme care will be taken to avoid damage to the wood and surrounding brick work or tiles. A variety of grades of sand paper will be used during removal and preparation of the surfaces for painting any secondary coats. Paint will be either burned off or scraped off dependant on the position keeping the safety of the property at all times and health and safety of the decorators. Individuals will wear appropriate H&S clothing at all times. Re-painting Using the materials indicated or equivalents, the house will have one coat of non pigment primer weather-shield followed by a coat of weather-shield undercoat and Dulux gloss overcoat. Once primers have cured exterior gloss paint will be applied to the area. Depending on the requirement a second coat or third coat maybe applied if required. Painting will be done in appropriate stages to take account of the drying process and to ensure all surfaces are correctly painted. Guttering will be removed, and replaced post paint having cured. When the repainting is completed and after a few days when paint is fully cured the guttering will be rehung, where pieces have perished new grey Osram guttering will be put in place. |