| 27 Upper Gordon Road Camberley Surrey GU15 2HJ Dismantling Technique | Chris Orkney HISTORIC BRICK MASON Shepperton cjo.hbm@gmail.com |
| --- | --- |
| Dismantling Boiler Flue |
| Description of operation: |
| Access via scaffold provided by client Initially cover roof with protective sheeting around the flue and then line with secondary cover of 50mm Insulation board to prevent damage from any debris Remove cowl and insert chimney balloon. Take note of materials within the flue to assess any substance deemed to be dangerous. Remove brickwork working course by course, using hand tools. Dampen down each course to reduce dust. All debris to be transported to ground level using a hoist for disposal or reclamation of brick. The flue is to be reduced to a level just above the highest point of roofline. The flue opening is to be sealed over with slate and covered with a lime mortar flaunching. If accidental damage to any roof tiles occurs, they will be replaced by a tile of similar size and colour. |