Design and Access Statement for repair and restoration of all 7 front (South) facing windows in Fuchsia Cottage, The Square, Kilkhampton, Bude, Cornwall. EX23 9QQ.

Fuchsia Cottage is a Grade II listed building, entry number 1328552, first listed on 29th September 1961. It is referred to as the ‘House adjoining the old Cartaret Arms at the West, The Square’

House, formerly part of poorhouse. (q.v. Cob Cottages and Hydeaway). C17, remodelled C19. Rendered, colourwashed slatestone rubble, slate roof, brick chimney at left end, chimney of local brick at right end adjoining room above cart entrance between this house and the Old Cartaret Arms. Early handmade ridge tiles above cartway. 2-storey 4 window range with off-centre entrance under sloping slate roof. Ground floor windows: three 2-light timber casements with slate sills, 6 panes per light, 8 panes per light on right. First floor windows : left, 2-light timber casement, 6 panes per light; middle, 3-light timber casement, similar panes; right, similar. Window above cart entrance 2-light timber casement, 6 panes per light. Interior not inspected.

Listing NGR: SS2532011415

The aim of the proposed work is to replace and repair rotten wood and restore the windows to the same visual appearance as they are currently in. They will retain the original features identically as they currently are, this being wooden frames and casements with the same profiles painted white and single pane glass, however the work will prevent wind and rain ingress which currently is a problem and is causing damp to penetrate through. It will also allow for the windows to be opened as currently 6 of the 7 windows do not open at all, painted or rotted shut, the only window opening is the top floor left hand side bedroom window. (Window 4) This work will also assist in the event of an emergency evacuation as currently there is a high risk of not being able to escape the property, if for example a fire was to block the front door egress. Allowing the windows to open will also assist with being able to clear the condensation that is inevitable with single pane glass, this is also contributing to premature rotting of the internal frames and windowsills and seeping into the cob walls causing damp. It will also reduce noise pollution inside the property and contribute to lessening the carbon footprint. The work will maintain the historic and architectural look and characteristics of the property and surrounding buildings. All access to the site will remain unchanged.

I have chosen Ventrolla to do the work as they have over 35 years’ experience of repairing and replacing casement windows and are top of their field in what they do. www.ventrolla.co.uk Separate drawings of the proposed new windows are attached to my application, with details of frame and glazing bar profiles. Repairs will follow the same design.

| Fuchsia Cottage viewed from the South. ‘House adjoining the old Cartaret Arms at the West, The Square’ |  |
| --- | --- |

| The Old Cartaret arms to the East and attached by the Drang Way to Fuchsia Cottage. |  |
| --- | --- |

Below is a photograph of each window with the description from the Technical Survey by Ventrolla of the work that needs to be carried out for each individual window. You will note the 3 downstairs windows need to be fully replaced while the 4 upstairs windows will be repaired.

| Item 1: Dressing Room Off Bathroom First Floor Front. Width: 1050 mm Height: 680 mm Casement window, left hand sash fixed, right hand opener. Both six pane. Both sashes and frame appear solid, r/h sash painted shut. NB sill is below 800mm. Comments: System: Casement Small (Top or Side Hung) Window Configuration: Casement Window New Sashes Right: Casement Sash Single Glazed 6 Pane Qty: 1 Hardware Hinges: Replace 2 Sets of Hinges Qty: 1 Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: |  |
| --- | --- |
| Item 2: L/H Master Bedroom First Floor Front Width: 1200 mm Height: 970 mm Casement three 6 pane sashes with centre opener. Opener painted shut but visually all appears solid. NB sill is below 800mm Comments: System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: 1 Left casement frame splice |  |
| Item 3: R/H Master Bedroom First Floor Front Width: 1200 mm Height: 940 mm. Original casement three 6 pane sashes with centre opener. Opener painted shut but visually all appears solid. NB sill is below 800mm Comments: System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: 1 |  |
| Item 4: Second Bedroom First Floor Front Width: 1020 mm Height: 1000 mm. Original casement window two 6 pane sashes, R/H opening. R/H Side of frame rotten to bottom and side. L/H sash has cables running through, appears solid. R/H sash also appears solid. NB sill is below 800mm Comments: System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Frame Repairs Top: Complete New Casement Frame - 2 Sash Sash Repairs Left: Conservation Joint Bottom Left Conservation Joint Bottom Right Right: Conservation Joint Bottom Left Conservation Joint Bottom Right Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: 1 |  |
| Item 5: Lounge Ground Floor Front Width: 970 mm Height: 1100 mm. Original casement window two 6 pane sashes, L/H opening. Both sashes and frame rotten through. NB sill is below 800mm Comments: System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Frame Repairs Top: Complete New Casement Frame - 2 Sash New Sashes Left: Casement Sash Single Glazed 6 Pane Qty: 1 Right: Casement Sash Single Glazed 6 Pane Qty: 1 Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Polished Brass Qty: 1 |  |
| Item 6: R/H Dining Room Ground Floor Front Width: 1000 mm Height: 1120 mm. Comments: Casement window two 6 pane sashes, L/H opening. Opener painted shut but both rotten outside as is frame. System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Frame Repairs Top: Complete New Casement Frame - 2 Sash New Sashes Left: Casement Sash Single Glazed 6 Pane Qty: 1 Right: Casement Sash Single Glazed 6 Pane Qty: 1 Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: 1 |  |
| Item 7: L/H Dining Room Ground Floor Front Width: 1000 mm Height: 1120 mm. Comments: Casement window two 8 pane sashes, R/H opening. Opener painted shut but both are rotten as is frame. System: Casement Small (Top or Side Hung) Window Configuration: Casement Window Frame Repairs Top: Complete New Casement Frame - 2 Sash New Sashes Left: Casement Sash Single Glazed 8 Pane Qty: 1 Right: Casement Sash Single Glazed 8 Pane Qty: 1 Hardware Casement Fittings: Crown Spoon-End Stay & Fastener - Antique Brass Qty: 1 |  |

The objective on completion of the work is to ensure the visual aspects of the building remain the same, maintaining its appearance and context in its conservation area and not affecting any surrounding buildings, while giving us widows that open and close. It will also contribute in preventing premature deterioration of the window areas of the building. I believe with the approach I have taken this will be achieved.