Arboricultural Impact Assessment

and

Arboricultural Method Statement

for

USAR,

Whitchurch Fire Station,

Whitchurch,

Cardiff.

Inspected by:-

Julian Wilkes BSc.For, MSc.Land Man, MIC.For, TechArb

Treescene Ltd

The Walled Garden

Old Coedarhydyglyn

St Nicholas

Cardiff

CF5 6SG

Tel No. 029 20599300

29th March, 2021

Registered Office:  Treescene Limited

The Walled Garden, Old Coedarhydyglyn, St. Nicholas, Cardiff CF5 6SG

Tel. 029 205 99300 Email. trees@treescene.co.uk

Arboricultural Impact Assessment

for

USAR,

Whitchurch Fire Station,

Whitchurch,

Cardiff.

Inspected by:-

Julian Wilkes BSc.For, MSc.Land Man, MIC.For, TechArb

Treescene Ltd

The Walled Garden

Old Coedarhydyglyn

St Nicholas

Cardiff

CF5 6SG

Tel No. 029 20599300

29th March, 2021

Registered Office:  Treescene Limited

The Walled Garden, Old Coedarhydyglyn, St. Nicholas, Cardiff CF5 6SG

Tel. 029 205 99300 Email. trees@treescene.co.uk

- BRIEF

I have been instructed by Mr Chris Evans of Lawray Architects to prepare an Arboricultural Impact Assessment (AIA) in relation to a proposed development at USAR, Whitchurch Fire Station, Whitchurch, Cardiff.

- TREE SURVEY AND PLAN

The information within this document is based on the Treescene Tree Survey dated 25.02.21 and the attached Treescene AIA Plan 03/2021.

- TREES TO BE REMOVED

a. Arboricultural Reasons

Trees T8, T9, T10, T11, G14 and T20 are recommended for removal in the Tree Survey due to poor quality (U category).

b. To Facilitate Development

Trees T1. T2, T3, T4, T5 and T6 are proposed for removal to accommodate the development layout.

These are all C category trees (low quality).

Trees to be removed are indicated on the attached Treescene AIA Plan 03/2021.

- TREE PRUNING

No tree pruning works are proposed at this point in time.

Should any remedial works  to improve tree safety or remove a potential source of nuisance be required in the future all pruning and felling/coppicing works are to be undertaken by suitably qualified and experienced Arboricultural Contractors working to BS3998:2010 Recommendations for Tree Work.

- ROOT PROTECTION AREA (RPA) INCURSIONS

There are no conflicts between proposed structures and RPAs of trees to be retained.

- PROTECTION OF RETAINED TREES

All trees to be retained should be protected by fencing in accordance with the details in BS5837:2012. The implementation of the tree protection on site should be in compliance with a site specific Tree Protection Plan (TPP) and Arboricultural Method Statement (AMS).

- IMPACT ON LOCAL AMENITY

Tree loss in relation to the development focuses primarily in the clearance of low quality trees in the interior of the site to create space to install the proposed new building. The existing robust tree group in the north western corner of the site as well as a group of conifers internal to the site are retained thus minimising any wider landscape impacts.

Extensive new tree planting within the northern boundary of the site is proposed thus mitigating any tree loss and contributing to an enhancement of the local tree stock as a result of the proposed development.

Arboricultural Method Statement

for

USAR,

Whitchurch Fire Station,

Whitchurch,

Cardiff.

Inspected by:-

Julian Wilkes BSc.For, MSc.Land Man, MIC.For, TechArb

Treescene Ltd

The Walled Garden

Old Coedarhydyglyn

St Nicholas

Cardiff

CF5 6SG

Tel No. 029 20599300

29th March, 2021

Registered Office:  Treescene Limited

The Walled Garden, Old Coedarhydyglyn, St. Nicholas, Cardiff CF5 6SG

Tel. 029 205 99300 Email. trees@treescene.co.uk

- BRIEF

I have been instructed by Mr Chris Evans of Lawray Architects to prepare an Arboricultural Method Statement (AMS) and a Tree Protection Plan (TPP) in relation to a proposed development at

USAR, Whitchurch Fire Station, Whitchurch, Cardiff.

- TREE SURVEY

The information in the AMS and TPP relates to the Treescene Tree Survey dated 25.02.21.

- TREES TO BE REMOVED

Trees to be removed are indicated in the Treescene Arboricultural Impact Assessment (AIA)             	29.03.2021.

- TREE PRUNING

No tree pruning works are proposed in relation to the development scheme.

- TREE PROTECTION PLAN

The position of the protective barriers is indicated on the enclosed Treescene TPP 03/2021. The tree 	protection will be installed immediately after the conclusion of the tree works and before the             	commencement of any construction activity on site.

6.   TREE PROTECTION BARRIERS

Protective barriers in accordance with BS5837:2012 and the enclosed drawing (Figure 2) will be       	installed in the locations indicated on the TPP under the supervision of the Arboricultural       	Consultant. The protective barriers will remain in situ until the completion of the construction work 	and final site landscaping.

No materials that are likely to have an adverse effect on tree health, such as oil, cement and bitumen 	will be stored or discharged within the protective barriers. No fires will be lit within 15m of the crown 	spread of retained trees and concrete will not be mixed or transported within 10m of the trunk of any 	tree.

7.	MONITORING AND SUPERVISION

The Arboricultural Consultant will undertake site inspections and monitoring/supervision at the 	following times:

a. 	Pre-commencement meeting with tree contractor to agree tree removal.

b. 	Supervision of installation of protective fencing.

c. 	Monitor condition of fencing every 4 weeks during construction.

d.  Supervision of removal of fencing following completion of project.

e.	Monitor condition of retained trees every 6 months following completion of construction for a                   	period of two years.