6th July 20201

Hull City Council

Planning

Guildhall

Alfred Gelder St

Kingston Upon Hull

HU1 2AA.

Dear Team,

Site:  ASK, WAREHOUSE 6, PRINCES DOCK STREET, KINGSTON UPON HULL,

HERITAGE STATEMENT

Heritage Category:

Listed Building

Grade:

II

List Entry Number:

1218969

Date first listed:

21-Jan-1994

Statutory Address:

WAREHOUSE AT SOUTH EAST CORNER OF PRINCE'S DOCK, PRINCE'S DOCK STREET

TA0928SE PRINCE'S DOCK STREET 680-1/25/313 (West side) Warehouse at south-east corner of Prince's Dock

GV II

Warehouse. c1830 and c1845. Brick with stone sills and hipped slate roofs. Plinth, rebuilt late C20. 3 storeys; 7x5 windows. Double range plan. Windows are mainly cast-iron glazing bar casements with slight segmental heads. South front, to Castle Street, has a central elliptical-arched loft door on the upper floors, flanked by 3 windows on each floor. Below, a central elliptical-arched carriage entrance with a pair of doors, flanked by single small blocked windows. To left, a similar carriage entrance, then a blocked window. Beyond, to right, 2 reglazed windows. Left return has 5 bays divided by shallow pilasters, and regular fenestration on the upper floors.

Right return has an elliptical-arched loft door to right on each of the upper floors, each flanked to left by a window. On the ground floor, 2 reglazed windows to the right and a small door to the left. Beyond, to right, a 3-bay section with shallow pilasters and regular fenestration on the upper floors. Below, 2 windows to right and to left, a door with blank fanlight.

Please refer to ASK Hull Visual Rev D and drawing nos: 596385-1,2 and block plan no: 596385-3.

2 SETS OF BUILT UP LETTERS – To replace existing. Letters have 1.2mm brushed brass face rims and returns.  Faces are set back within the return for an open trough effect.  Bull nosed 15mm opal 030 acrylic lines push through the faces.  Rebated 10mm opal 030 acrylic backs are fitted with low energy white LEDS for face and halo illumination.  Backs are screw fixed to 30x30mm SHS horizontal rails which are finished similar to the brickwork and which fix to the brickwork.

1 INTERNALLY ILLUMINATED MENUS – To replace existing. Internally illuminated. Folded and soldered 1.2mm brushed brass box with a hinged access door.  Window is fitted with 6mm toughened glass.  Steel hinge and chrome lock. Fret cut text is backed with 5mm opal 030 acrylic.  Fitted with low energy white LEDs in the top recess.  Screw fixed to the wall.

Our design team has looked at all aspects of creating a signage scheme to suit the Grade II listed building. We have always been aware to produce a design concept that compliments the surrounding conservation area and is sympathetic to the listed building. We feel our simple design and method of illumination bodes well with the building.

In view of the fact that we are not making an adverse changes to the building and we are only replacing signage like for like and using where possible all existing fixtures and fittings there will be absolutely no detrimental impact to the heritage assets of the building.

Access

Not applicable. Our application relates to signage / adverts only and the painting of the facade.  There will be no change to the current access arrangements as part of this application.