Application for Listed Buildings Consent

Design and Access Statement      August 2021

Mistley Church Hall, New Road, Mistley CO11 1ER

The proposals relate to a single storey Church Hall built in 1911 to a design by

W. D. Caroe (1857 – 1938).  Caroe was well known, associated with the Arts & Crafts movement, architect to a number of cathedrals, designer of many churches and the headquarters of the Church Commissioners, No.1 Milbank, London.  For many years this building has served both the needs of the Parish and the local community.  During WWII the building was requisitioned and a single storey extension added incorporating toilet facilities.  Its use during this period remain unclear.  It was handed back in 1946.

After an application to Historic England by a third party it was listed Grade II in 2016.

Now in 2021 it is necessary to make some repairs to the fabric.  These will repair damage to the kitchen ceiling from a water leak, the rear doors were damaged during a break-in, water leaking through the roof of the WWII extension requires investigation and remedy, hopefully by simple renewal of the seals around the fixing bolts.  In all three cases we aim to replace what is damaged by material that is the same as what has been removed.

Recently fly-tipping has occurred through the unrestricted access to the site.  This has resulted in 170 truck tyres and discarded double mattresses being dumped on site, not withstanding unauthorised parking if the hall is not in use.  Apart from being unsightly it has proved expensive to rectify.  The gap in the hedge, together with the dropped kerb, is 5.18 metres wide.  We propose to install two collapsible bollards in the gap to prevent unauthorised vehicle entry.  With the bollards folded flat (once unlocked) authorised vehicle entry is straight forward over the bollards.  Pedestrian access at all times is unaffected.  Off road parking for authorised people using the hall is also unaffected

Joy L Baker