Schedule of Works  - Mount Pleasant Farm – Offton

Listed building application – DC/22/02997

Application for installation of window opening on west elevation of property.

- Work has already commenced on removal of existing render on west elevation of farmhouse. This work commenced under authority of listed building consent DC/22/01054. Sand and cement render on wire mesh removed from wooden frame of building, leaving oak studs exposed. Attached plans and photographs show opening as it now is.

- If approval granted for works, a timber frame window will be commisioned that would be in keeping with all other fenestration within the listed building. Details of the proposed window are included within the application . Glazing of said window would also match all other glazing within building.

- On receipt of window frame it would be attached to the outside of the oak studs in the position as specified on all drawings. This work would be completed by experienced builder who is currently engaged on restoration project. No change whatsoever will take place to existing oak frame. Window and it's openings would be in place of concrete render that was present on the walls.

- After window is fixed in position it would be finished and made watertight by the abutment of wood wool boards finished with a render of  Thermalime, an overlay of fine lime, and finished with a limewash paint. All these works are as per finish on rest of house as detailed in original application DC/22/01054.