Design and Access Statement

Proposed Residential Development at 128 Great Haylers Road Hengrove Bristol

Introduction and Environment

This statement is in support of the planning application for a two storey side extension to form 2no 1 bedroom self contained flats including associated access and parking

The existing property comprises a two storey end of terrace house located on the junction of Great Haylers Road and Tarnock Avenue and has brick elevations and gabled tiled roof. There is an existing single storey rear garage accessed from Philippa Close and there is a large side garden

To the North on the opposite side of Great Haylers Road are the rear gardens of the properties fronting onto Tarnock Avenue and these comprise two storey residential properties with brick elevations and tiles gabled roofs.

To the West are the other properties forming the terrace formed by 114-128 and these are similar residential properties with brick elevations and tiled gabled roof

To the South are the properties access from Charter Walk and these are too far from the application site to be affected

To the East is a section of open land and on the opposite side of Great Haylers Road are the rear gardens of the properties Tarnock Avenue

There is a wide variety of materials in the vicinity of the site including, brick, render with tiled roof. Windows are predominantly white pvc u

The site is within a central location and will have easy access to public transport on Walsh Avenue and is within walking distance to Whitchurch shopping centre

There are also local schools and parks within walking distance and therefore the site can be assumed to be in a very sustainable location and within an urban area.

Design and Access Statement

Proposed Residential Development at 128 Great Haylers Road Hengrove Bristol

Means of Access

The site fronts onto both Great Haylers Road and Philippa Close and the existing properties has a garage and parking space in front of the garage off Philippa Close

The proposal is to form a new access off Great Haylers Road to provide 2no car parking spaces each min 2.4 x min 5.1m and will be allocated to the new flats and the existing garage and parking space will be allocated to No 128

There will be a bin store formed in the front by the drive for ease of access on collection day for No 128 and the new flats

There will be shed in the rear garden of No 128 and the rear garden of the ground floor flat and a bike bunker in the front garden of the first floor flat proposed flats for bike store

The site can be accessed by a fire appliance on Great Haylers Road and be within 45m of any part of the building therefore no need to enter the site

Access will comply with the building regulations in regard to disable access

The site is well located to public transport with bus stops on Walsh Avenue giving good access to Bristol City Centres and is within walking distance of Whitchurch Shopping Centre

Design and Access Statement

Proposed Residential Development at 128 Great Haylers Road Hengrove Bristol

The Proposal

The application is a full application for 2no one-bedroom self contained flats in a two storey side extension fronting onto Great Haylers Road with associated access and parking

Density

In the site location there is a mixture of housing types which is predominantly terraces and semi semi detached houses and this proposal is of a similar density and provide a mixture of accommodation

Layout

The proposed is in the form of a two storey side extension following the building line along Great Haylers Road with private amenity space to the rear for No 128 and the ground floor flat and a single storey extension to no 128 which would normally far within permitted development

The main aspects will be to the north and south which will not cause any overlooking issues to adjoining properties

Appearance

The proposed is follow the front elevation of No 128 with similar cladding panel between the ground and first floor windows and tiled gable roof with a two storey rear projection which follows the line of a single storey rear extension to 128

The proposed materials will be brick with white pvcu cladding between the windows and tiles that will match the existing used in the area and white pvc u windows and doors

Design and Access Statement

Proposed Residential Development at 128 Great Haylers Road Hengrove Bristol

Sustainability and Drainage

The site is current wide side garden and the proposal will incorporate soakaways for storm drainage and permeable paviors to drives so the proposal will be to provide a reduction in discharge to the sewer system.

All drive will slope away from the adopted highway. There will be PV panels used in conjunction with air source heating to reduce the carbon reduction

Foul drainage will consist of gravity system discharging to the existing on site drainage system which connects to the existing sewer which is located in the rear garden

Conclusion

The proposal is seeking to make better use of a large side plot and does not cause any overlooking or over bearing issues and replicates the building line along Great Haylers Road

The proposal provides covered and secure cycle storage that complies with your standards

The proposal provided bin storage for each flat next to the site entrance for ease of access on collection day.

The proposed of street parking complies with your authorities standards

The proposal incorporated private amenity spaces which exceed your authorities standards

I trust this proposal meets with your approval