Proposal for tree work within a Conservation Area.      20/10/2023

Applicant name:-	Dr Brian Dale

Location: -		19 Dreghorn Loan, Edinburgh EH13 0DF

We submit this notification of proposed work on behalf of Dr Brian Dale.

The trees along the boundary to the south east of the property are in the garden of 21 Dreghorn Loan, and overhang the applicant’s garden.

Proposed Works

The details of the work are set out below. Wherever possible, the trees will be pruned to maintain their appearance and to leave them with a natural form. Final pruning points will be in accordance with BS3998:2010 'Tree Work - Recommendations', reducing branches to appropriate pruning points.

A plan of the area is included with the trees identified using the item numbers below.

1 - Horse Chestnut

This tree is growing in the neighbour's property at 21 Dreghorn Loan.

Height 13m, spread 14m, DBH 750mm.

The tree shows signs of historic pruning with associated Some of the large pruning wounds are unlikely to occlude. Our ground based VTA survey could not identify if there are decay pockets at these pruning points.

A hazard beam is developing in a contorted branch of around 20cm diameter, at around 8 metres above ground level. Several areas of the crown have become over extended, arising from new vigorous growth from previous (historic) pruning points.

Reduce spread to the west, north and east by around 1.5 to 2m radius. Reduce height by 1 to 1.5m, shortening the over extended branches by around 2 metres to bring them back into line with the remaining crown.

Reduce the length of the branch with the hazard beam by around 1.5 metres to reduce loading on the compromised section.

2 – Lime

The tree is growing to the east of the Horse Chestnut (T1), in the neighbour's property at 21 Dreghorn Loan.

Height 17m, spread 11m, DBH 720mm.

The tree appears to be in generally good condition.

Moderate dead wood present at 6m and 10m.

Reduce height by 2 to 2.5 metres, pruning to suitable subordinate branches. This will maintain the tree at a suitable size for the location, and avoid excessive shading of the applicant’s garden and greenhouse.

Also, remove the moderate dead wood and sever the Ivy at the base of the tree.

3 - Holly

The trees are growing around the base of the Lime (T2), and in the neighbour's property at 21 Dreghorn Loan.

H3.5 - 4m, S 7m, DBH multi stem 15 - 90mm

Reduce height to around level with the trellis in order to return it to forming a hedge.

Trim the face back to the line of the boundary.

The pruning will be carried out in accordance with British Standard  3998:2010 'Tree Work - Recommendations', reducing branches to appropriate pruning points.

Prepared by Duncan Brooks

Duncan Brooks & Colette Walker

Directors

Associate Member of The Arboricultural Association.

PGDip., Cert. Arb. L4 (ABC), NCHort.

# Text boxes

ROOT & BRANCH ARBORICULTURE Ltd.

Professional Tree Services