Planning Statement

Relating to discharge Condition 7

Two storey side and rear extension to include ground floor shop extension and two number new apartments at first and second floor, including flat roof section

At

184b Haslucks Green Road, Shirley,

Solihull, B90 2LN

Introduction

This Planning statement has been prepared to discharge condition 7 relating to application ref PL/2022/01404/PPFL

Description of Planning Condition

Condition 7. Before the use hereby approved commences, any commercial to residential areas shall be insulated in accordance with a scheme agreed in writing by the Local Planning Authority. Details approved shall be implemented and retained thereafter.

Design Proposed to be discharged-

The insulating scheme on the first floor is as follows:

- Floor cover (carpet/karndean)

- Underlay

- Mutemat 8mm thick

- 22mm T&G floor boards

- 200mm acoustic slab insulation between posi joists

- 12.5mm acoustic plasterboard to the underside of posi joists

- 12.5mm fire rated plasterboard fitted over the acoustic boards

- Resilient bars for suspended ceiling with 150mm void

- Suspended ceiling system with 600x600mm ceiling tiles