Materials

Planning Application – Extension of porch - Silver Jade GL128EB

Roof

Re-fit existing clay pan tiles on 50mm x 25mm roofing batons.

On breathable felt

On 150mm x 50mm treated timbers at 400 centers.

Fit 150mm Celatex in roof space.

Exterior Walls

12.5mm Douglas Fir live edge cladding

0n 50mm x 25mm batons

On breathable felt

On 12.5mm OSB board glued and screwed to all 150mm x 50mm timbers at 400 centers.

150mm Celetex in all external walls.

Interior

Floor – 100mm concrete on DPM on 100mm Celatex.

Walls – 12,5mm OSB glued and screwed to all timbers. Fit 12.5mm plaster board and skim.

Doors – UPVC double glazed

Window – UPVC double glazed fire escape.